EE403/503 Introduction to Plasma Processing

Examples solutions

Test 1: Basic Atomic Theory

Example 1. How fast is an Electron and a Hydrogen atom at room temperature?

Electrons:         	me = 9.1 x 10-31 Kg

k = 1.38 x 10-23 J/K (Boltzmann’s Constant)

T = 293K

Hydrogen:				mH = 1.66 x 10-27 Kg

k = 1.38 x 10-23 J/K (Boltzmann’s Constant)

T = 293K

Example 2. In the vacuum tube shown in the figure below, determine the location, velocity and energy of e, H and H+ at the time when the electron arrives at one of the electrodes. All three particles are initially at rest.

me = 9.1 x 10-31 Kg

k = 1.38 x 10-23 J/K (Boltzmann’s Constant)

T = 293K

Time for electron arrives at the anode t

(x = distance travel)				 (E = Electric Field)

2

(    (

Electron:

Location : at the anode

Velocity:

Energy:

Ion:

Location:

= 0.5 mm from the center toward cathode

Velocity:

Energy:

Atom:

Location: 			 at the center

Velocity:				 at rest

Energy:

Example 3. Using the Bohr’s model, write a program to:

(1) Calculate the five lowest energy states including the ground state of hydrogen atoms in eV.

(2) Calculate the ionization potential of hydrogen atoms in eV.

(3) Find the energy states of hydrogen atoms that can absorb photons with wavelengths in the visible range (400-700 nm).

(1):

n = 1		E1 = 0

n = 2		E2 = 10.19 (eV)

n = 3		E1 = 12.08 (eV)

n = 4		E1 = 12.74 (eV)

n = 5		E1 = 13.05 (eV)

(2):

RH = 13.6 eV    n1 = 1		n2 = (

(3):

| Series |  | (eV) | (nm) |
| --- | --- | --- | --- |
| Lyman | 1(2 | 10.20 | 121.32 |
|  | 1(3 | 12.09 | 102.37 |
|  | 1(4 | 12.75 | 97.06 |
|  | 1(5 | 13.06 | 94.78 |
| Balmer | 2(3 | 1.89 | 655.15 |
|  | 2(4 | 2.55 | 485.29 |
|  | 2(5 | 2.86 | 433.30 |
| Paschen | 3(4 | 0.66 | 1871.85 |
|  | 3(5 | 0.97 | 1279.58 |

# Text boxes

Visible wavelength